# Questions you should ask when purchasing CCTV systems.

## What is the objective?

  - What do you need to see?

  - What are the images to be used for (as evidence in a criminal trial, deterrence etc)?

## How is this to be achieved?

  - Cameras in specific areas

    - Are cameras indoors or outdoors?

    - Is the subject to be viewed back-lit (silhouetted against the light source)?

    - Can the cameras be vandalised or attacked easily?

    - Are two cameras required; to watch each other should there be a chance they could be vandalised.

    - Outdoor weatherproof housings must have heaters. Do they need washers/wipers as well?

    - Is there a stable support structure available on which to mount the camera? (un-stayed poles such as power, telephone, flag and flood lights tend to sway in the wind)

  - Is suitable lighting at the infrared end of the spectrum available? (Mercury Vapour discharge lamps are not suitable)

  - Are infrared illuminators required?

  - Are specialist “starlight” or low-light cameras required?

## Cameras must have a minimum resolution

  - 450 TV Lines (TVL).

## Lens and camera processing technology

  - Must be suitable to provide evidential images under all lighting conditions with respect to location.

## Camera classification

  - A” type = Standard indoor use with controlled lighting.

    - 450 TVL,  min. 1 lux,

    - Auto shutter,

    - Varifocal lens,

    - controlled lighting environment,

    - no vandal resistant housing

- “B” type = Indoor/outdoor where lighting is affected by daylight, camera pans and/or tilts. If outside, a heated weatherproof housing is fitted and suitable mounting is required for high wind loading and “ball” strikes.

    - 450 TVL, min. 0.5 lux,

    - auto shutter,

    - Varifocal lens

    - indoor/outdoor with weatherproof housing and heater.

- “C” type = cameras for use in difficult conditions where the subject is backlit, or, with significant variations in background lighting, or, day/night in areas of lower outside evening light levels, where the camera goes from colour to monochrome increasing its sensitivity.

    - 450 TVL, min. 0.2 lux

    - auto shutter,

    - varifocal lens,

    - special feature camera; backlight or Day/Night etc.

    - indoor/outdoor with weatherproof housing, heater, wiper/washer.

## How are the images to be displayed?

  - Locally on video monitors?

  - Locally on selected computer terminal?

  - Remotely on computer terminals?

## Power supply

  - Is the system required to operate in the event of mains power failure?

  - If the answer is yes, for how long and what illumination is required?

## Recording devices

  - Video capture cards in PC’s are not acceptable

  - All images to be stored on DVR with embedded operating system and dedicated video capture.

  - DVR is to have a 15-25% spare input capacity.

  - Capture rate in frames per second to be stipulated.

  - Resolution is to be 640x480 or higher.

## Cable

  - All camera supply cables and video cables to be supplied and installed as per the Ministry of Education intruder alarm specifications dated June 2000 clause 10.

## Installation of the CCTV system

  - To be carried out by suitably qualified installers holding current membership of the NZSA Inc. (New Zealand Security Association) and licensed under the Private Investigators & Security Guards Act 1973.